AMATEUR RADIO TRAINING
FOUNDATION
Propagation
Release: v2.101
hamtrain.co.uk

---
Propagation
Radio Waves
The Ionosphere
HF
VHF / UHF

---
Radio Waves
Travel in straight lines
Can be reflected, or refracted/diffracted (‘bent’)
Get weaker as they get further from the transmitter
Distance depends on a number of factors:
    - Antenna
    - Frequency
    - Power
    - Obstructions
    - Conditions

---
The Ionosphere
Layer of conductive gases between 70 and 400km above the Earth.
Ionisation is mainly caused by ultraviolet rays from the Sun
VHF and UHF signals pass through this layer
HF signals are refracted (‘bent’) back to Earth

---
Ionosphere and HF
The Ionosphere ‘refracts’ HF signals, allowing world-wide contacts beyond line-of-sight
Light refraction

---
HF Bands
HF bands are “open” (e.g. support Skywave propagation) at different times of the day and the year.
Each HF band is affected differently.
Solar activity has a big effect on the Ionosphere
Contact around the world is done using multiple “hops”
Multiple hop

---
VHF / UHF
The range of VHF and UHF is less than that of HF
  - Typically limited to “just beyond line-of-sight”
The range decreases as the frequency increases
At VHF/UHF frequencies, radio waves get weaker when penetrating buildings. Glass is more transparent to radio waves.
Snow, ice and heavy rain can “attenuate” signals (i.e. reduce the power) at UHF and above.

---
VHF / UHF
VHF and UHF can be blocked by obstructions, hence antennas are normally located outdoors at high points
Hills can cause radio “shadows”
Outdoor antennas are preferable to indoor / loft antennas

---
VHF / UHF
The range of VHF/UHF is dependant on:
  - Antenna height
  - Antenna gain (using a beam antenna)
  - A clear path
  - Transmitter power
Higher antennas are preferable to higher power as they improve both transmit and receive performance.

---
VHF / UHF
The range of VHF/UHF can be extended by some atmospheric conditions:
  - VHF/UHF pass through the Ionosphere but propagation can occur through the Troposphere (which is below the Ionosphere)
  - “Sporadic E” and “Atmospheric ducting” can increase the range of VHF/UHF signals

---
Summary
  - The Ionosphere is a layer of conductive gases between 70 and 400km above the Earth
  - HF signals travel around the world – refracted by the Ionosphere
  - VHF/UHF is generally “just beyond line-of-sight”
  - At VHF/UHF, height is more important than power

---
Propagation
Got a question?
Ask your tutor, or go to sxham.uk/help
HamTrain.co.uk
© EssexHam.co.uk